## Slide 1: EE 521/ECE 582 – Analysis of Power systems
Class #8 – September 20, 2022
Dr. Noel N. Schulz
Edmund O. Schweitzer III Chair in
Power Apparatus and Systems
Chief Scientist Joint Appointment, PNNL
Co-Director, PNNL/WSU Advanced Grid Institute (AGI)
Washington State University Pullman
Noel.Schulz@wsu.edu EME 35
509-335-0980 (o) and 509-336-5522 (c)

## Slide 2
Student Hours
Office Hours This Week
  Tuesdays 4:30-5:30 pm (after class) - Zoom
  Wednesdays 4-5 pm Zoom or EME 35 Pullman
  Fridays 1:30-2:30 pm Zoom or EME 35 Pullman
Join from PC, Mac, Linux, iOS, or Android: https://wsu.zoom.us/j/8237216735 (Links to an external site.)
Meeting ID: 823 721 6735
Or by request via email noel.Schulz@wsu.edu or phone 509-336-5522

## Slide 3: Check In Meetings
Remaining ones – Wednesday and Friday
Checking your work – Example on Page 90 of textbook (3 bus) and example in notes (4 bus)
14 Bus Cases
  Do not use Tap values for first part of work (will discuss next week)
  Do a few Y bus calculations by hand and compare to your program (including Y99)
Will post information from check-in meetings in discussions on Canvas

## Slide 4
Numerical Differentiation
Another quasi-Newton approach is to approximate the individual entries of the Jacobian through numerical differentiation. Consider the slope of f(x) evaluated at a:
Let h be a small difference in x, then
is the backward difference approximation
is the forward difference approximation
is the center difference approximation

## Slide 5
Even more complex methods of numerical differentiation are possible. The following is the Richardson approximation:
However the amount of computation required for the derivative approximation must be weighed against the increase in accuracy.
No Quasi-Newton method will exceed the full Newton-Raphson in convergence speed.

## Slide 6
Newton-Krylov Methods
In the previous Quasi-Newton methods, it was assumed that linearized iterates were ultimately solved using a direct method. However, there is no reason why this should be. In fact, it is possible by combining a Newton-Raphson iteration (outer) with an iterative linear solver (inner), that computational gains may be achieved, especially for solvers such as the GMRES method.
Furthermore, the GMRES requires only the vector product of the Jacobian with a vector, which can be approximated using a difference method. This approach is called a Jacobian Free GMRES method.

## Slide 7
Jacobian-Free Newton-GMRES Algorithm for Solving f(x) = 0

## Slide 8
Use difference approximation

## Slide 9
Example:
Solve
Let h = 10-3,  = 10-3 , and

## Slide 10
h
h
h
h
This is the vector product that replaces calculating the Jacobian
Difference approximation
We have this from above

## Slide 11
Complete GMRES iteration
Since the error is larger than the convergence tolerance, the inner loop is repeated.

## Slide 12
Inner loop has converged, therefore proceed

## Slide 13
This is the first update of the outer loop
This outer error is too large, so the entire process (both inner and outer iterations) is repeated
After convergence
There errors are nearly identical to the original Newton-Raphson solution
The potential savings from using a Jacobian-Free Newton-GMRES method arise from not having to calculate the system Jacobian at every step. Furthermore, it is possible that the GMRES iteration may not require a full number of iterations (k < n) as xq approaches convergence.

## Slide 14
Continuation and Homotopy Methods
In many physical systems, the problem defined by the mathematical equation f(x) = 0 may in some way depend in a natural way on a parameter smoothly varying λ of the system.
λ may be a parameter such as temperature, load, or pressure
When λ is set equal to 0, the system f0(x) = 0 has a known solution x0. However, for varying λ, and entire family of functions H(x, λ) exist such that:
H(x,0) = f0(x) and H(x,1) = f(x)
where a solution x0 of H(x,0)=0 is known, and the equation H(x,1) = 0 is the desired problem to be solved.

## Slide 15
In other words, the homotopy method slowly morphs the problem f0(x)=0 into the problem f(x)=0 as λ goes from zero to one.
In most cases, f0(x)=0 is a well-defined problem with an easy to compute solution.
The function f(x)=0 may be difficult to solve due to either difficult to estimate initial conditions, or perhaps a region in which the Jacobian is ill-conditioned.

## Slide 16
Example: Morph the system of equations
into
Solution (2,3)
Solution (-3,2)

## Slide 17
A Homotopic function:
At
The homotopic function is solved via a predictor/corrector step:
The predictor step takes the form:

## Slide 18
Predictor step at every step i:
NR Corrector step at every step i where x(k=0) =xi
Derivative/Jacobian of f(x) and f0(x)

## Slide 19
Example again: Solve the system of equations
using the homotopic mapping from

## Slide 20
Define:
With

## Slide 21
Then the prediction step:

## Slide 22
Correcting using Newton-Raphson:
After the NR converges:
Then repeat for i = 2, 3, etc. until  = 1.0
The results as  are as shown next.

## Slide 23
x1, x2 = (2,3),  = 0
Set of equations at  = 0

## Slide 24
x1, x2 = (-3,2),  = 1

## Slide 25
x1, x2 = (2,3)
x1, x2 = (-3,2)
Progression of x1 and x2 as  goes from 0 to 1

## Slide 26
Homotopy is used when the original system may become ill-conditioned. The Jacobian of the merged systems remains non-singular even when the Jacobian of the original system becomes singular:
May be singular
Newton-Raphson
Homotopy
Non-singular

## Slide 27
Power System Applications

## Slide 28
Find the voltage magnitudes, phase angles, and line flows for the small power system with the following system parameters in per unit:
Knowns:
Bus | Type | V | PG | QG | PL | QL
1 | Slack | 1.02 | -- | -- | 0.0 | 0.0
2 | PV | 1.00 | 0.5 | -- | 0.0 | 0.0
3 | PQ | -- | 0.0 | 0.0 | 1.2 | 0.5
i | j | Rij | Xij | Bij
1 | 2 | 0.02 | 0.3 | 0.15
1 | 3 | 0.01 | 0.1 | 0.1
2 | 3 | 0.01 | 0.1 | 0.1
Bus data
Line data
Bus 3:
Independent
Unknowns:
P3,inj and Q3,inj
V3 and 3
Bus 2:
P2,inj and V2
2
Bus 1:
V1 and 1
none

## Slide 29
Find admittance matrix Y:
i | j | Rij | Xij | Bij
1 | 2 | 0.02 | 0.3 | 0.15
1 | 3 | 0.01 | 0.1 | 0.1
2 | 3 | 0.01 | 0.1 | 0.1
Line data
This is capacitive line charging: put ½ of Bij at each node i and j

## Slide 30
Jacobian:
In radians, not degrees!
Error= = 1.1802

## Slide 31
Repeat for iteration 2 – update Jacobian and mismatch:
Error= = 0.0359

## Slide 32
Repeat for iteration 3 – update Jacobian and mismatch:
Error= = 0.0009084
Converged!

## Slide 33
Calculate Dependent Unknowns:
Slack bus powers

## Slide 34
What Y terms are affected if Line between 1 and 5 is opened?
What Y terms are affected if I add a capacitor bank to Bus 3

## Slide 40
Regulating Transformers in Power Flow
Put in admittance matrix form:
Y(i,j)
Y(j,i)
Y(j,j) no change
add to Y(i,i)

## Slide 41
If the voltage at bus j is regulated, the voltage magnitude Vj becomes a known value and the tap setting t is now the unknown.
Another approach is to let directly solve for t from the Newton-Raphson. All partial derivatives with respect to Vj are replaced with derivatives with respect to t
Pros and Cons for each approach?

## Slide 42
Decoupled Power Flow
Recall that the Jacobian does not need to be exact for the NR to still converge rapidly.
Consider the power flow Jacobian:
The generic form of is
The generic form of is
If the transmission lines are primarily reactive, then ij is  90o. Furthermore, adjacent bus angles are usually within a few degrees,
Therefore and

## Slide 43
Therefore
Advantages:
  Matrices are smaller, therefore decreasing LU factorization effort
  V and  iterations are performed separately and may converge independently (i.e. different number of iterations)
Disadvantages:
  Convergence may be slow if system is not well-conditioned (i.e. zero assumption is not valid)
Many commercial programs have the option to switch between full and decoupled NR iterations.

## Slide 44
Revisit previous example:
This
Is smaller than this
This
Is smaller than this
Separate solutions:
Very close to full NR!
Continue until convergence…

## Slide 45
Fast Decoupled Power Flow
In the previous decoupled power flow, the Jacobian was updated at every iteration. If the Jacobian is held constant at every iteration, the method is known as the “Very Dishonest Newton’s Method.” This method still requires at least one Jacobian evaluation.
However, another approach in which the Jacobian is a constant matrix is called the fast decoupled power flow. In this case, the Jacobian is approximated based on the line parameters.
Variations include the XB, BX, XX, and BB methods.
The XB and BX are the most common.

## Slide 46
XB version:
Approximation to
Approximation to
where and is the shunt susceptance at bus i

## Slide 47
Revisit previous example again:

i | j | Rij | Xij | Bij
1 | 2 | 0.02 | 0.3 | 0.15
1 | 3 | 0.01 | 0.1 | 0.1
2 | 3 | 0.01 | 0.1 | 0.1
Line data

## Slide 48
Compare sub-Jacobians:
Fast Decoupled
Sub-Jacobian at Flat Start
Very close to full NR!
Continue until convergence…
Iterate:

## Slide 49: Programming Projects:
Power Flow Project (20%)
  Ybus, Jacobian matrices – Newton Raphson
  LU Factorization, Backward-Forward substitution for NR
  Fast Decoupled
  Q-limits, transformer taps

## Slide 50: Announcements
Finish Reading Chapter 3
Extra Video will drop Friday
MATLAB Program
  Input the CDF file – Start with Data in Program
  Start working on building the Ybus
  Calculate Jacobian Matrix Values
  Work on LU Decomposition and Solution
  Next Add Tap Changing feature
  Start working on Fast Decoupled
See example on Page 90 to check your work